## Slide 1
FPGA Fundamentals

## Slide 2
What is an FPGA?
Field Programmable Gate Array.
Contains:
  Logic gates
  Registers
  Configurable Routing
  Memory (RAMs, ROMs)
  PLLs
  Arithmetic & DSP
  Hard IP Blocks
Fully programmable.

## Slide 3
Configurable Logic Block (CLB)
Look Up Table
D Type
Flip Flop
MUX
Clock
Reset
A
B
C
D
F
CLB

## Slide 4
Simplified FPGA Architecture
FPGA IO PINS
IO
IO
IO
IO
IO
PLL
RAM
CLB
Programmable Routing
CLB
CLB
CLB

## Slide 5
Why Use An FPGA?
Used for implementing Digital Systems.
Extremely Flexible.
  No limit to timers, counters, peripherals etc.
  Does not have a fixed hardware structure.
  Change whole design without changing layout.
Very fast.
Parallel processing (Doesn’t execute sequentially).
Large bandwidth (Data width configurable).
Intensive data processing (Video, DSP, FFT etc)

## Slide 6
When Not To Use An FPGA
In cost sensitive applications.
Carrying out infrequent tasks that are sequential in nature (eg : search / sort algorithms).
When speed and latency are not that important.

## Slide 7
FPGA Programming
Hardware Description Languages (HDL)
C/C++ using HLS (High Level Synthesis)
Popular HDL Languages :
VHDL | Verilog
Strongly Typed | Weakly Typed
Deterministic | Only Deterministic If you Follow Rules Carefully.
Verbose | Concise
Non C Like Syntax | More C Like Syntax

## Slide 8
RTL (Register Transfer Level)
Can be simulated, synthesised & implemented on an FPGA.
Describes hardware in terms of registers and combinational logic that sits between them.
Need to have an idea of the digital circuit.
No explicit delays.
All timing described in terms of clock edges.
Used as input to a synthesis tool.

## Slide 9
FPGA Design Flow
Start from the Design Specification
Use Verilog HDL Editor To :
  Write Verilog HDL (RTL)
  Write Test-Bench
Simulate to ensure correct behaviour.
Write Timing Constraints.
Synthesis tool to generate a netlist.
Implementation tool to take netlist and perform placement, routing and optimisation.
Make sure designs meets Timing. If not go back to VHDL code.
Implementation creates a binary file used to configure the FPGA.

## Slide 10
FPGA Design Flow
Program binary file into FPGA configuration flash (using JTAG for example)
FPGA
Config Flash
JTAG Programmer
JTAG Port

## Slide 11
Chapter Summary
Configurable Logic Block (CLB)
FPGA Architecture
When to use an FPGA?
What are FPGAs good at?
When might you not use an FPGA?
Overview of FPGA programming languages.
Typical FPGA design flow.